## Slide 1: How to use a micropipette
Autumn Becker and Ryan mccann

## Slide 2: Micropipette anatomy

## Slide 3: Before we begin
First identify the range of the micropipette (max and min)
  Ask if you can’t figure it out!
When you eventually set the micropipette volume, DO NOT spin the top wildly, be controlled and mature
When not using the micropipette for work, do not spin the dial, as this can lead to a ruined micropipette.
If you accidentally exceed the limits of the micropipette, DO NOT press down

## Slide 4: First Activity for today
Starting with larger micropipettes, begin transferring green water from the beaker onto the wax paper. The volumes that everyone in the group should be using are as follows:
  With the 200µL-1000µL pipette: 1000µL, 500µL, 200µL
  With the 100µL-1000µL pipette: 800µL, 300µL, 150µL
  With the 20µL-200µL pipette: 200µL, 75µL, 20µL
  With the 10µL-100µL pipette: 95µL, 23µL, 18µL
  With the 2µL-20µL pipette: 19µL, 11µL, 3µL
  With the 0.5µL-10µL pipette: 9.6µL, 4.2µL, 0.8µL

## Slide 5: Second Activity for today
Your group will be attempting to pipet a total of 25ml from the beaker of green water, into a separate beaker. Using each pipet at least once, and making sure everyone in the group goes, create a plan to complete the task.
How will you know if you did it right? Weigh it!
25mL*(1g/1ml)=25g